AVL  User Primer                                 last update  3 July 1998
Mark Drela, MIT Aero & Astro


AVL (Athena Vortex Lattice) was originally written by Harold Youngren
circa 1988 for the MIT Athena TODOR aero software collection.  A number 
of modifications have since been added by Mark Drela and Harold Youngren.


Input file
----------
AVL takes one input file which describes the vortex lattice geometry.
The geometry is described in the following Cartesian system:

  X   downstream
  Y   out the right wing
  Z   up

The freestream must be at a reasonably small angle to the X axis, 
since the trailing vorticity is oriented parallel to the X axis.


The input file begins with the case information in the first 5 lines:

ABCD...                    | case title, uppercase to plot properly
#                          | comment line begins with "#" or "!"
0.0                        | Mach
1     0     0.0            | iYsym  iZsym  Zsym
4.0   0.4   0.1            | Sref   Cref   Bref
0.1   0.0   0.0            | Xref   Yref   Zref

Mach  = freestream Mach number (< 1) for Prandtl-Glauert correction
iYsym =  1  case is symmetric about Y=0    , (X-Z plane is a solid wall)
      = -1  case is antisymmetric about Y=0, (X-Z plane is at const. Cp)
      =  0  no Y-symmetry is assumed
iZsym =  1  case is symmetric about Z=Zsym    , (X-Y plane is a solid wall)
      = -1  case is antisymmetric about Z=Zsym, (X-Y plane is at const. Cp)
      =  0  no Z-symmetry is assumed (Zsym ignored)
Sref  = reference area  used to define force coefficients (CL, CD, CM, etc)
Cref  = reference chord used to define pitching moment (CM)
Bref  = reference span  used to define roll,yaw moments (CR,CN)
X,Y,Zref = location about which moments and rotation rates are defined

Only the half (non-image) geometry must be input if symmetry is specified.
Ground effect is simulated with iZsym = 1, and Zsym = location of ground.

Forces are not calculated on the image/anti-image surfaces. 
Sref and Bref are assumed to correspond to the total geometry.


The remainder of the file consists of a set of keywords and associated
data.  Each keyword expects a specific number of lines of data to 
immediately follow it.  The keywords must also be nested properly 
in the hierarchy shown below (only the first four characters of each 
keyword are actually significant, the rest are just a mnemonic),

  SURFACE
      YDUPLICATE
      HINGE
      CONTROL
      TRANSLATE
      ANGLE

      SECTION
          NACA

      SECTION
          CAMBER

      SECTION
          AIRFOIL

      SECTION
          CFILE

      SECTION
          AFILE
          DESIGN

  SURFACE
      YDUPLICATE

      SECTION

      SECTION

  SURFACE
     .
     .
      etc.


The YDUPLICATE, HINGE, CONTROL, TRANSLATE, and ANGLE keywords can all 
be used together.  If more than one of these appears for a surface, 
the last one will be used and the previous ones ignored.

At least two SECTION keywords must be used for each surface.  Also, 
these must appear after any YDUPLICATE,HINGE,CONTROL,TRANSLATE,ANGLE 
keywords.

The NACA, CAMBER, AIRFOIL, CFILE, AFILE keywords are alternatives.  
If more than one of these appears after a SECTION keyword, the last 
one will be used and the previous ones ignored.  i.e.

  SECTION
    NACA
    CAMBER
    CFILE

is equivalent to

  SECTION
    CFILE


*****

SURFACE            | (keyword)
Main Wing          | surface name string
12   1.0           | Nchord  Cspace

The SURFACE keyword declares that a surface is being defined until 
the next SURFACE keyword, or the end of file is reached.  A surface 
does not really have any significance to the underlying AVL vortex 
lattice solver, which only recognizes the overall collection of all 
the individual horseshoe vortices.  SURFACE is provided only as a 
configuration-defining device, and also as a means of specifying
surface deflections (described later).  Also, partial forces are 
calculated and displayed separately for each surface.  This is 
necessary for load calculations, for example.

Nchord =  number of chordwise horseshoe vortices placed on the surface
Cspace =  chordwise vortex spacing parameter (described later)

*****

YDUPLICATE      | (keyword)
0.0             | Ydupl

The YDUPLICATE keyword is a convenient shorthand device for creating 
another surface which is a geometric mirror image of the one being 
defined.  The duplicated surface is _not_ assumed to be an 
aerodynamic image or anti-image, but is truly independent.  
A typical application would be for cases which have geometric 
symmetry, but not aerodynamic symmetry, such as a wing in yaw.  
Defining the right wing together with YDUPLICATE will conveniently 
create the entire wing (as two separate surfaces, though).

The YDUPLICATE keyword can _only_ be used if iYsym = 0 is specified.
Otherwise, the duplicated real surface will be identical to the
implied aerodynamic image surface, and velocities will be computed
directly on the line-vortex segments of the images.  This will 
almost certainly produce an arithmetic fault.

If the hinge axis for the current surface is (X Y Z), then the
the hinge axis for the duplicate surface is (X -Y Z).  The two
surfaces will then move opposite (like ailerons) when the same 
hinge deflection angle is specified interactively.  Symmetric 
(elevator or flap) movement is specified via hinge angles
of opposite sign.  

Ydupl =  Y position of X-Z plane about which the current surface is 
         reflected to make the duplicate geometric-image surface.

*****

HINGE             | (keyword)
 0.0  1.0  0.0    | X,Y,Z hinge-axis vector  (any scale)

The HINGE keyword defines the hinge axis about which the 
surface (its normal vectors, actually) is to be deflected
interactively during program execution.  If omitted, 
a default axis will be defined to extend from the first 
to the last section, lying in the Y-Z plane.

*****

CONTROL           | (keyword)
 2                | number of control-variable lines to follow
 E  1.0           | delta_e declaration, d(hinge_deflection)/d(delta_e)
 R  2.0           | delta_r declaration, d(hinge_deflection)/d(delta_r)

The CONTROL keyword declares that an additional hinge deflection for this 
surface is to be governed by one or more control variables.  Up to six 
different control variables can be selected, indicated by the following
key characters.

 key   variable    intended use , primary control action
 ---   --------    -------------------------------------
  A     delta_a      aileron    ,      x moment
  E     delta_e      elevator   ,      y moment
  R     delta_r      rudder     ,      z moment
  T     delta_t      thrust     ,      x force
  Y     delta_y      side force ,      y force
  F     delta_f      flaps      ,      z force

The control derivatives will be generated for all variables 
which are declared.


More than one variable can contribute to the motion of a surface.
In the example above, the surface total surface deflection will 
be the result of two contributions on top of the basic manual 
hinge deflection:

added_hinge_deflection  =  1.0 x delta_e  +  2.0 x delta_r

This can be used to simulate control mixing.  The following 
is a typical definition for both halves of a V-tail, where 
delta_e is the symmetric deflection the tails, and delta_r
is the antisymmetric deflection, in a 1:2 proportion.

SURFACE 
Right Tail
CONTROL
 2
 E  1.0
 R  2.0
.
.

SURFACE
Left Tail 
CONTROL
 2
 E -1.0
 R  2.0


These declarations assume that the hinge vectors point from root 
to tip for each tail.  This "mirror" reflection of the hinge
vector is the definition used by YDUPLICATE, and is also the default 
definition.  When the duplicate surface is created, some of the
d(hinge_deflection)/d(delta) coefficients are negated to produce
the expected action, as given by the table below.

     as defined         =>        duplicated
 --------------------        --------------------
  d(hinge)/d(delta_a)         d(hinge)/d(delta_a)
  d(hinge)/d(delta_e)        -d(hinge)/d(delta_e)
  d(hinge)/d(delta_r)         d(hinge)/d(delta_r)
  d(hinge)/d(delta_t)        -d(hinge)/d(delta_t)
  d(hinge)/d(delta_y)         d(hinge)/d(delta_y)
  d(hinge)/d(delta_f)        -d(hinge)/d(delta_f)

Hence, the definition 

SURFACE
Right Tail
YDUPLICATE
0.0
CONTROL
 2
 E  1.0
 R  2.0

is equivalent to defining both right and left sides explicitly
as in the previous example.


*****

TRANSLATE         |  (keyword)
10.0  0.0  0.5    | dX  dY  dZ

The TRANSLATE keyword allows convenient relocation of the entire 
surface without the need to change the Xle,Yle,Zle locations for 
all the defining sections.

dX,dY,dZ =  offset added on to the Xle,Yle,Zle values for all the
            defining sections in this surface.

*****

ANGLE       |  (keyword)
2.0         | dA

The ANGLE keyword allows convenient changing of the incidence angle 
of the entire surface without the need to change the Ainc values 
for all the defining sections.

dA =  offset added on to the Ainc values for all the defining sections
      in this surface

*****

SECTION                              |    (keyword)
0.00  0.00  0.00  0.50 1.00  5 -2.0  | Xle Yle Zle Chord Ainc Nspan Sspace

The SECTION keyword defines an airfoil-section camber line at some 
spanwise location on the surface.

Xle,Yle,Zle =  airfoil's leading edge location
Chord       =  the airfoil's chord  (trailing edge is at Xle+Chord,Yle,Zle)
Ainc        =  incidence angle, taken as a rotation (+ by RH rule) about 
               the surface's spanwise axis projected onto the Y-Z plane.  
Nspan       =  number of spanwise vortices until the next section
Sspace      =  controls the spanwise spacing of the vortices
       (Nspan and Sspace for the last section in the surface are ignored)

Note that Ainc is used only to modify the flow tangency boundary 
condition on the airfoil camber line, and does not rotate the geometry 
of the airfoil section itself.  This approximation is consistent with 
linearized airfoil theory.

The local chord and incidence angle are linearly interpolated between
defining sections.  Obviously, at least two sections (root and tip)
must be specified for each surface.

The default airfoil camber line shape is a flat plate.  Four keywords,
described below, are available to define non-planar camber lines.  
If one of these is used, it must immediately follow the data line
of the SECTION keyword.

All the sections in the surface must be defined in order across the span.

*****

NACA                      |    (keyword)
4300                      | section NACA camberline

The NACA keyword sets the camber line to the NACA 4-digit shape specified

*****

CAMBER                    |    (keyword)
20                        | N
0.0   0.0                 | x/c(1)  y/c(1)
0.1   0.002               | x/c(2)  y/c(2)
 .     .                  |  .       .
 .     .                  |  .       .
 .     .                  |  .       .
1.0  -0.01                | x/c(N)  y/c(N)

The CAMBER keyword declares that the camber line definition is input
as a set of x/c, y/c pairs.

N       =  number of points to follow
x/c,y/c =  camber line coordinates 

The x/c, y/c pairs are splined, and the slope of the y(x) function
is used to modify the flow tangency condition in the same manner as
the overall incidence Ainc.  To avoid extrapolating the spline, the
x/c values should run from 0 to 1.  The y/c values do not need to
be 0 at either endpoint.

*****

AIRFOIL   X1  Y1          |    (keyword)
20                        | N
0.0   0.0                 | x/c(1)  y/c(1)
0.1   0.002               | x/c(2)  y/c(2)
 .     .                  |  .       .
 .     .                  |  .       .
 .     .                  |  .       .
1.0  -0.01                | x/c(N)  y/c(N)

The AIRFOIL keyword declares that the airfoil definition is input
as a set of x/c, y/c pairs.

N       =  number of points to follow
x/c,y/c =  airfoil coordinates 

The x/c, y/c coordinates run from TE, to LE, back to the TE again 
in either direction.  These corrdinates are splined, and the slope 
of the camber y(x) function is obtained from the middle y/c values 
between top and bottom.  The rest of the treatment is as for CAMBER.

If present, the optional X1 X2 parameters indicate that only
the x/c range X1..X2 from CFILE is to be assigned to the surface.
If the surface is an 20%-chord flap, for example, then X1 X2
would be 0.80 1.00.  This allows the camber shape in CFILE to be 
easily assigned to any number of surfaces in picewise manner.


*****

CFILE      X1  X2         | (keyword)   [ optional x/c range ]
filename                  | filename string

The CFILE keyword is essentially the same as CAMBER, except
that the x/c,y/c pairs are read from the file "filename".
The number of points N is not specified explictly anywhere.

The optional X1 X2 parameters are used as in AIRFOIL.


*****

AFILE      X1  X2         | (keyword)   [ optional x/c range ]
filename                  | filename string

The AFILE keyword is essentially the same as CAMBER, except
that the x/c,y/c pairs are generated from a standard (XFOIL-type)
set of airfoil coordinates contained in the file "filename".  
The first line of this file is assumed to contain a string
with the name of the airfoil (as written out with XFOIL's SAVE
command).

The optional X1 X2 parameters are used as in AIRFOIL.


*****

DESIGN                  | (keyword)
Nline                   | number of lines to follow
Kdes  Wdes              | variable index,  variable weight
Kdes  Wdes              | variable index,  variable weight
Kdes  Wdes              | variable index,  variable weight
Kdes  Wdes              | variable index,  variable weight
 .                           .
 .                           .


This declares that the section angle Ainc is to be virtually 
perturbed by some number of design variables, each having index
Kdes and weight Wdes.  For example, the declaration

DESIGN
 3
1  3.0
4  2.0
5  1.5


specifies that the total virtual angle of the section is

  Ainc_total = Ainc  +  3.0*D_1  +  2.0*D_4  +  1.5*D_5

where D_1, D_4, D_5 are design variables.

The sensitivities of the flow solution to design variable changes
can be displayed at any time during program execution.  Hence,
design variables can be used to quickly investigate the effects
of twist changes on lift, moments, induced drag, etc.

The ability to superimpose design variables for any section angle
allows the design variables to represent convenient "design modes",
such as linear washout, which influence all sections.


*****

CDCL                         |  (keyword)
CL1 CD1  CL2 CD2  CL3 CD3    |  CD(CL) function parameters


The CDCL keyword specifies a simple profile-drag CD(CL) function 
for this section.  The function is parabolic between CL1..CL2 and 
CL2..CL3, with rapid increases in CD below CL1 and above CL3.
See the SUBROUTINE CDCL header (in cdcl.f) for more details.

The CD(CL) function is interpolated for stations in between
defining sections.  Hence, the CDCL declaration on any surface 
must be used either for all sections or for none.


****************************

Spacing Parameters -- Sspace, Cspace

These parameters must fall in the range  -3.0 ... +3.0 , and they
determine the spanwise and chordwise horseshoe vortex distributions
as follows:

 parameter                              spacing
 ---------                              -------

    3.0        equal         |   |   |   |   |   |   |   |   |

    2.0        sine          || |  |   |    |    |     |     |

    1.0        cosine        ||  |    |      |      |    |  ||

    0.0        equal         |   |   |   |   |   |   |   |   |

   -1.0        cosine        ||  |    |      |      |    |  ||

   -2.0       -sine          |     |     |    |    |   |  | ||

   -3.0        equal         |   |   |   |   |   |   |   |   |

          spanwise:      first section        ==>       last section
          chordwise:     leading edge         ==>       trailing edge

An intermediate parameter value will result in a blended distribution.
The most efficient distribution (best accuracy for a given number of 
vortices) is usually the cosine (1.0) chordwise and spanwise.  If the 
wing does not have a significant chord slope discontinuity at the 
centerline, such as a straight, elliptical, or slightly tapered wing, 
then the -sine (-2.0) distribution from root to tip will be more 
efficient.  This is equivalent to a cosine distribution across the 
whole span.  The basic rule is that a tight chordwise distribution 
is needed at the leading and trailing edges, and a tight spanwise 
distribution is needed wherever the circulation is changing rapidly, 
such as taper breaks, and especially at flap breaks and wingtips.

If a surface airfoil camber line has a significant discontinuity 
in the slope due to flap deflection, say, it may be appropriate
to define the surface as two separate surfaces each with its own 
cosine distribution.  This will bunch points at the hinge line, 
giving good accuracy.  Separate definitions are needed anyway if 
the flap is to be deflected independently of the wing.


Execution
---------

AVL is executed with the input filename as an argument:

  % avl filename


After the geometry input is processed and the vortex lattice is
constructed, the aero influence coefficient (AIC) matrix is factored,
and the induced velocity matrix is constructed.  The user is then
put into an operating menu which is mostly self-explanatory:

==============================================
  M ach  number
  R oll  rate       A lpha           
  P itch rate       B eta            
  Y aw   rate       C lear all       
 -------------------------------------  
  H inge defl.      I mage side      
  CO ntrol defl.
  DE sign mod.      O ptions         
 -------------------------------------  
  G eometry plot    T refftz plane plot
 -------------------------------------- 
  D  stab. derivs   VB strip Vz, My  
  SE nsitivities    RE ference data  
  FT total forces   FN surface forces  
  FS strip forces   FE element forces
  Q uit             W rite forces to file

 Select action:  


In general, if an operating variable (alpha, beta, roll rate, etc.)
or a surface deflection is specified, it will remain fixed at that 
value until it is specified again, or cleared via the C command.

Anytime a command is given to specify an operating variable, such 
as B for beta (yaw angle), the prompt will display the current value:

 Enter beta (deg)  (999 to trim CN):   8.0000

Just hitting <return> will take the current 8.0 value as the default
response.

As indicated in the prompt, any operating parameter can also be
indirectly specified by requesting that the associated moment
be driven to zero.  Each moment component is associated with 
a parameter as follows:

  pitch moment CM  <=>  alpha, pitch rate
    yaw moment CN  <=>  beta ,   yaw rate
   roll moment CR  <=>          roll rate

More than one moment can be trimmed simultaneously, but a moment
cannot be trimmed "twice" --- e.g. 999 cannot be specified for 
both alpha and pitch rate.

Trimming the pitching moment coefficient CM is a very easy way
to determine the trimmed CL value for each surface.  By repeatedly
deflecting the tail surface, say, a trimmed-CL versus tail setting
line can be generated very quickly.  The W command will write
all the surface deflections and surface CLs to disk for convenient 
later perusal.  Each time the W command is issued, the name of the 
output file will be requested, with the previous filename (if any)
shown as the default:

 Enter summary output file: file.out

Just hitting <return> will result in the present conditions and 
forces being appended to this file.  If another filename is entered, 
the previous file will be closed and the new file will be created.
The summary output file can be read with program TRIM and plotted
(although this program is somewhat ad-hoc at present).

Another typical application for the trimmed-moment options might 
be for example to determine the effect of sideslip or aileron
deflection on the steady roll rate.


Besides allowing moment trimming, the alpha command A in addition 
allows the total CL to be specified:

 Enter Alpha        (deg):    2.0000
       CL (to specify CL):    0.8000
       CM (to trim pitch)


Entering "CL" will produce the CL prompt:

 Enter specified CL:   0.8000

which also offers the current specified-CL value as the default.



Output
------

Everytime an operating parameter is specified, the integrated forces 
are displayed for the entire configuration and the individual surfaces.
The loads on the individual vortex elements can be displayed with the 
E command, but this is rather voluminous and often not very informative.

The force and moment directions are in stability axes x,y,z, which 
are tilted up by the angle alpha from the body axes X,Y,Z:

 | x |     | cos(a)    sin(a)| | X |
 | y |  =  |        1        | | Y |
 | z |     |-sin(a)    cos(a)| | Z |


The following standard normalizations are used.

 CD = F_x / (q Sref)            drag
 CY = F_y / (q Sref)            side force
 CL = F_z / (q Sref)            lift

 CR = M_x / (q Sref Bref)       roll  moment
 CM = M_y / (q Sref Cref)       pitch moment
 CN = M_z / (q Sref Bref)       yaw   moment

The CD,CY,CL forces are positive in the direction of the x,y,z axes, 
respectively.  Likewise, the moment components CR,CM,CN are positive 
about the x,y,z axes by righthand rule. 

The roll, pitch, and yaw rates (WX,WY,WZ) input from the operating 
menu are defined in the body axes.  This convention was chosen for 
the greatest programming simplicity rather than some aerodynamic
tradition.  The stability-axes rates Wx,Wy,Wz are easily obtained 
using the  x,y,z <= X,Y,Z  transformation matrix shown above.
The reverse transformation is simply the inverse of this matrix:

 | WX |     | cos(a)   -sin(a)| | Wx |
 | WY |  =  |        1        | | Wy |
 | WZ |     | sin(a)    cos(a)| | Wz |



It must be pointed out that if sideslip (beta) is nonzero, then
CD and CY are not the true "drag" and "side-force" aligned with
the relative wind direction.  Likewise for CR and CM.  The
wind-axes directions are given by

 | x |          | cos(b) sin(b)    | | x |
 | y |       =  |-sin(b) cos(b)    | | y |
 | z |_wind     |                1 | | z |

                | cos(b)cos(a)   sin(b)   cos(b)sin(a)| | X |
             =  |-sin(b)cos(a)   cos(b)  -sin(b)sin(a)| | Y |
                |      -sin(a)     0            cos(a)| | Z |

hence

 CD_wind =  CD cos(b) + CY sin(b)
 CY_wind =  CY cos(b) - CD sin(b)
 CL_wind =  CL

 CR_wind =  CR cos(b) + CM sin(b)
 CM_wind =  CM cos(b) - CR sin(b)
 CN_wind =  CN


AVL does not display these wind-axes forces since they are not
relevant to stability and control calculations, and differ from the 
stability-axes forces only if a steady-state sideslip is present, 
such as perhaps in a steady turn.  The primary quantity of interest 
here is the overall L/D = CL_wind/CD_wind = CL/CD_wind, and CD_wind 
is more accurately obtained from the Trefftz-Plane anyway.

The alternative Trefftz-Plane drag coefficient CDi is calculated 
from the wake trace in the Y-Z plane far downstream.  This is 
generally more reliable than the CD obtained from surface force 
integration, and is the appropriate wind-axes induced drag for 
performance prediction.

The span efficiency is defined as
         2                             2
 e  =  CL  / (pi A CDi)    ;   A = Bref / Sref

with Sref being replaced by  2 Sref  for Y-image cases (iYsym = 1).


Stability derivatives
---------------------

Command D generates the stability derivative matrix for the
current conditions.  The derivatives are expressed entirely
in the AVL stability axes (both the forces as well as rates).
Note that the AVL and the "traditional" stability axes differ
in having the x and z directions reversed.  

Plotting
--------

The T command starts up the Treffts Plane plot menu:

 ======================================================
   Y plot data vs Y
   Z plot data vs Z
   D ownwash angle toggle
   L imits for plot
   R eset plot limits
   N umber surfaces
   A nnotate plot
   H ardcopy current plot
   ZM zoom
   U nzoom
   S ize change

 Select option for Trefftz plane plot (or <return>): 

These plot options are self-explanatory.


The G commands starts up the geometry-plotting menu which allows 
viewing of the horseshoe vortex lattice and other geometric features.

 ==============================================
  K ey commands (viewpoint, zoom...)          

  H ardcopy current plot      A nnotate plot  
  O ptions                    S elect surfaces

  CH ordline   T     CA amber        F
  CN tlpoint   F     TR ailing legs  F
  BO ound leg  T     NO rmal vector  F
  HI nge axes  F     LO ading plot   F

 Select option (or <return>):  


The K command enters a sub-sub menu which allows rotation of the 
aircraft to a suitable viewing angle, zooming, distortion for
perspective, etc.

  ------------------------------------------------
  Type keys in graphics window...

    L eft             R ight        (Azim. Psi  ) 
    U p               D own         (Elev. Theta) 
    T ilt z axis      S et upright  (Bank  Phi  ) 
    C lear

    Z oom on curs.    N ormal size    
    I ngress          O utgress       
    H ardcopy         J ot annotations

  ...<space> to exit  
  ------------------------------------------------

These commands must be typed with the cursor in the graphics window,
and their action is performed immediately.  All other menus work in
the usual text window.